1. Выбрал так же протокол HSRP, добавил R3 в standby с аналогичными настройками

2. Схема сети в Eve-NG

3. Так же выбрал Standby HSRP.
PC HQ office
auto eth0
iface eth0 inet static
address 192.168.0.10
netmask 255.255.255.0
gateway 192.168.0.254

SW1 без настроек
R1
interface GigabitEthernet0/0
 ip address 192.168.0.1 255.255.255.0
 standby 1 ip 192.168.0.254
 standby 1 priority 110
 standby 1 preempt
 duplex auto
 speed auto
 media-type rj45
!
interface GigabitEthernet0/1
 ip address 10.1.0.1 255.255.255.252
 duplex auto
 speed auto
 media-type rj45

ip route 0.0.0.0 0.0.0.0 10.1.0.2

R2
interface GigabitEthernet0/0
 ip address 192.168.0.3 255.255.255.0
 standby 1 ip 192.168.0.254
 standby 1 priority 105
 standby 1 preempt
 duplex auto
 speed auto
 media-type rj45
!
interface GigabitEthernet0/1
 ip address 10.3.0.1 255.255.255.252
 duplex auto
 speed auto
 media-type rj45

ip route 0.0.0.0 0.0.0.0 10.2.0.2

R3

interface GigabitEthernet0/0
 no ip address
 shutdown
 duplex auto
 speed auto
 media-type rj45
!
interface GigabitEthernet0/1
 no ip address
 standby 1 ip 192.168.0.254
 standby 1 priority 101
 standby 1 preempt
 shutdown
 duplex auto
 speed auto
 media-type rj45

ip route 0.0.0.0 0.0.0.0 10.3.0.2

NGFW

interface GigabitEthernet0/0
 ip address 10.3.0.2 255.255.255.252
 duplex auto
 speed auto
 media-type rj45
!
interface GigabitEthernet0/1
 ip address 10.2.0.2 255.255.255.252
 duplex auto
 speed auto
 media-type rj45
!
interface GigabitEthernet0/2
 ip address 10.1.0.2 255.255.255.252
 duplex auto
 speed auto
 media-type rj45
!
interface GigabitEthernet0/3
 ip address 10.4.0.2 255.255.255.252
 duplex auto
 speed auto
 media-type rj45
!
ip forward-protocol nd
!
!
no ip http server
no ip http secure-server
ip route 192.168.0.0 255.255.255.0 10.1.0.1
ip route 192.168.0.0 255.255.255.0 10.2.0.1
ip route 192.168.0.0 255.255.255.0 10.3.0.1
ip route 192.168.1.0 255.255.255.0 10.4.0.1

ISP Rostelecom

interface Loopback0
 ip address 10.10.10.10 255.255.255.252
!
interface GigabitEthernet0/0
 ip address 10.4.0.1 255.255.255.252
 duplex auto
 speed auto
 media-type rj45
!
interface GigabitEthernet0/1
 ip address 10.5.0.1 255.255.255.252
 duplex auto
 speed auto
 media-type rj45
!
ip forward-protocol nd
!
!
no ip http server
no ip http secure-server
ip route 192.168.0.0 255.255.255.0 10.4.0.2
ip route 192.168.1.0 255.255.255.0 10.5.0.2
ip route 0.0.0.0 0.0.0.0 10.10.10.10

R4

interface GigabitEthernet0/0
 ip address 10.5.0.2 255.255.255.252
 duplex auto
 speed auto
 media-type rj45
!
interface GigabitEthernet0/2
 ip address 192.168.1.1 255.255.255.0
 duplex auto
 speed auto
 media-type rj45
!
ip forward-protocol nd
!
!
no ip http server
no ip http secure-server
ip route 0.0.0.0 0.0.0.0 10.5.0.1

SW без настроек

PC Fillial
auto eth0
iface eth0 inet static
address 192.168.0.10
netmask 255.255.255.0
gateway 192.168.1.1